## Slide 1
DIGITAL LOGIC DESIGN
8-to-3 Priority Encoder
Theory • Logic Circuit • Logisim Simulation
TEAM MEMBERS
R. Geethika Chowdary | 2620040043 Kanamata Srikari | 2620030701 Ganugapati Venkata Sushanth Sri Ram | 2620040012 Bikkina Karunakar | 2620040038
8 INPUTS → 3 OUTPUTS
D7
D6
D5
D4
D3
D2
D1
D0
ENCODER
Y₂ Y₁ Y₀
Section: __________
Prepared for Digital Logic Design project presentation

## Slide 2
01 • INTRODUCTION AND OBJECTIVE
What is an 8-to-3 Priority Encoder?
02
INTRODUCTION
A priority encoder converts 8 input lines into a 3-bit binary output.
If several inputs are HIGH, it selects only the highest-priority active input.
D₇ HIGHEST • D₀ LOWEST
OBJECTIVES
1
Understand priority selection
2
Convert the selected input to binary
3
Design and test the circuit in Logisim
Key idea: the highest active input wins.

## Slide 3
02 • THEORY AND LOGIC CIRCUIT
Priority rule and logic gates
03
WORKING RULE
The highest active input wins.
Example: D₆ = 1 and D₃ = 1. D₆ wins because it has higher priority.
Output = 110
NOT • AND • OR gates implement priority masking and binary encoding.
FUNCTIONAL CIRCUIT BLOCK
D7
D6
D5
D4
D3
D2
D1
D0
PRIORITY MASKING
Y₂ Y₁ Y₀
8 input lines → priority logic → 3-bit output
Simplified functional diagram; gate-level wiring is built in Logisim.

## Slide 4
03 • CIRCUIT DESIGN IN LOGISIM
Build and test the circuit
04
IMPLEMENTATION STEPS
1
Place 8 input pins D₀–D₇
2
Add NOT, AND and OR gates
3
Connect priority masking logic
4
Add output pins Y₂, Y₁, Y₀
5
Use the pin tool to test inputs
LOGISIM CIRCUIT LAYOUT GUIDE
D7
D6
D5
D4
D3
D2
D1
D0
AND / OR
ENCODE
Y₂ Y₁ Y₀
Replace this guide with a screenshot of your actual Logisim circuit.
Working: higher-priority inputs mask lower inputs before the 3-bit output is generated.

## Slide 5
04 • SIMULATION RESULTS
Input-output combinations and truth table
05
EXAMPLE TEST CASES (D₇ HAS THE HIGHEST PRIORITY)
Inputs D₇…D₀ | Selected | Output | V
10000001 | D₇ | 111 | 1
01000100 | D₆ | 110 | 1
00100100 | D₅ | 101 | 1
00001010 | D₃ | 011 | 1
00000001 | D₀ | 000 | 1
00000000 | None | 000 | 0
ANIMATED EXAMPLE
When D₆ and D₃ are HIGH, D₆ wins.
Output = 110
V = 1 means at least one input is active. Capture your own Logisim tests for final submission.

## Slide 6
05 • CONCLUSION AND APPLICATIONS
Outcome, uses, and possible improvements
06
CPU INTERRUPTS
Select the most urgent processor request.
BUS ARBITRATION
Choose among devices sharing a bus.
CONTROL SYSTEMS
Give precedence to critical signals.
DIGITAL SYSTEMS
Encode selected requests into binary.
Conclusion: 8 inputs are encoded into 3 bits representing the highest-priority active input.
Possible improvements: add a Valid output, test all priority cases, and extend to more inputs.
THANK YOU